## Slide 1: Civil Engineering project river flood
Mia Hajjar
Hady Souaiby
Jerome Chaker
Yoanna Maroun

## Slide 2: Plan
01
Introduction and problem statement
Models and training
04
Data collection and sources
02
Levfeature engineering and methodology
03
Results and evaluation
05
System architecture and conclusion
06

## Slide 3: Introduction & Problem
03
Flooding = major natural disaster
02
Focus: river gauge stations in the US
Real-time flood risk prediction system
01
05
Need for accurate & fast predictions
04
Key Question
can we predict whether a river will flood tomorrow?

## Slide 4: Project Overview
Covers 11 river stations
Uses real government data (USGS + NOAA)
Outputs predictions via: REST API and Interactive dashboard
End-to-end Machine Learning pipeline

## Slide 5: Data Sources
USGS
River discharge (2018-2026)
01
NOAA
Weather data:
-Precipitation
-wind
-temperature
-snowfall
02

## Slide 7: Target & Risk Levels
3-class classification:
Normal (< 75%)
Medium (75%–90%)
High (> 90%) → flood risk
Thresholds different per river
Example:
Potomac: 28,540 cfs
Cherry Creek: 211 cfs

## Slide 8: Feature Engineering
38 engineered features:
Discharge history (lags)
Rolling averages
Seasonal patterns
Weather variables
01
Data split:
02
75%
15%
15%
03
No random shuffle (time series logic)

## Slide 9: Models
Baseline
Logistic Regression
Advanced
LightGBM
LightGBM
300 trees
Learning rate =0.05
Handles class imbalance

## Slide 10: Lead-Time Results
Prediction accuracy
1 day: 0.686 (best)
3 days: 0.481
7 days: 0.224
Best reliability
1–2 days ahead

## Slide 11: System Architecture
Python
Backend:
01
Health (status)
Latest (recent data)
Predict (risk levels)
Predict-stage (water level)
Endpoints:
02

## Slide 12: Dashboard
Station selection
01
Flood probability display
03
Real-time data loading
02
Charts & diagnostics
04
Built with Next.js
Features:
Stage forecast
02

## Slide 13: Monitoring
01
Detects data drift
02
Alerts when retraining needed
03
Ensures model reliability over time

## Slide 15: Conclusion
4
Useful for engineers and emergency planning
3
Real-time system deployed
2
Reliable next-day predictions
1
LightGBM model performs well
5
Covers 9 river stations